## Slide 1: Smart Stepper
2023 - 2024 OIT Wilsonville Junior Project designed by:
Ismael Hernandez-Hernandez Zachary Elliott Ian Gaffney Cari Blaker
WITH BIOFEEDBACK FOR TOE-WALKERS

## Slide 2: WHAT IS TOE-WALKING?
Problematic gait
Causes further health issues
Affects 5% of the population
Physical therapy doesn't help
Surgery ineffective
The world needs a solution!

## Slide 3: SOLUTION REQUIREMENTS
Shoe senses gait
  Feedback for improvement
    Stealthy; medical capability disguised
      Encouragement to heel strike (for kids!)
        Shareable with parents & medical professionals

## Slide 4: Smart stepper solution
The Smart Stepper is a shoe featuring:
4 embedded piezoelectric sensors
Embedded haptic vibrator (live feedback)
Smart watch connection with a week of data feedback/display

## Slide 5: HARDWARE
Seeed Studio Microcontroller: - small enough to be encapsulated by shoe comfortably - supports analog input (with enough pins) from piezoelectric sensors - supports BLE connection - internal battery, plus external battery & its charging support - plenty of on-chip and on-board memory
Four Piezoelectric sensors:
  provide feedback voltage
  save on power
3.7V battery
Haptic Vibrator : provides live feedback by vibrating on toe strikes
Bangle.JS 2.0 Smart Watch - BLE capability
- fully programmable
PER SHOE
PER PROJECT

## Slide 6: HARDWARE Encasement
Thermoplastic Polyurethane (TPU) Filament
12% Infill
182 grams used
3D Printing

## Slide 7: SEEED BOARD
KiCad EDA
jlcpcb
FLEX

## Slide 8: CIRCUIT bOARD

## Slide 9: SOFTWARE
Device | IDE | Language
Fusion 360 | CAD | N/A
Prusa Printer | PrusaSlicer | Gcode
Seeed studio microcontroller | Arduino IDE | Arduino
Bangle.JS 2.0 | Espruino's Web IDE | JavaScript
KiCad EDA | s-expression schematic | N/A

## Slide 10: SOFTWARE

## Slide 11: Graph Display
Foot Class
+good +bad +total +bottom_steps +top_steps +bottom_color +top_color +x_start +x_finish +y_bottom_start +y_top_start +y_bottom_finish +y_top_finish +update(good, bad)
Bar Class
+day +date +day_relation +file_contents +left foot +right foot +highest_total +parse_file(contents) +update()

## Slide 12: costs
Product | Units | Price Per | Cost Per Project
Bangle.JS 2 Smart Watch | 1 | $93.22 | $93.22
Seeed Studio Microcontroller | 2 | $15.99 | $31.98
3.7V Lithium Ion Battery | 2 | $14.95 | $29.90
Piezo Electric Sensor | 10 | $0.79 | $6.32
Haptic Vibrator | 2 | $1.20 | $2.40
Shoes (pair) | 1 | $60.00 | $60.00
Filament TPU Roll (0.75 Kg) | 1 | $29.99 | $14.99
Total Physical Cost |  |  | $238.81

## Slide 13: schedule
This term:
  Read/Write data
  Bluetooth Connection
  Data histogram display
  Board Creation
  3D Insoles printed
  Testing
Spring term:
  Idea Fest preparation
  PCB board order
  Rigorous testing and refining
  Game creation
  Insole changes—waterproofing!
  Phone app
  Game
  BLE completion
  Adding sensor arrays for accuracy

## Slide 14: Are you ready for a demonstration?!

## Slide 15: Thank you