OREGON INSTITUTE OF TECHNOLOGY
Computer Systems Engineering Technology Department
CST 204 – Introduction to Microcontrollers
Final Exam

Name: ________Cari Blaker______________________________

1) What do the serial communication acronyms DTE and DCE stand for?

DTE:____Data Terminal Equipment __________________________________________________	(2 points)

DCE:______________Data Circuit-terminating Equipment ________________________________________	(2 points)

2) Circle correct answer - A terminal is a DTE / DCE device.	(2 points)

3) Circle correct answer - A computer system with a RS-232 port is a DTE / DCE device.	(2 points)

4) Circle correct answer - A telephone computer modem is a DTE / DCE device.	(2 points)

5) Indicate the correct DTE/DCE sense for the serial communications interface shown below (PIN, Socket) by circling the appropriate choice (DTE or DCE).	(5 points)

        PIN Socket

        DCE / DTE DCE

6) Show the direction of the TXD (transmit data/data send) signal with an arrow on the pin/socket interface shown above in question 6.	(5 points)

7) Assume the logic level signal below (8N1) is received by a UART serial port (time axis goes from left to right).

a) Highlight the start bit, and the stop bit (assume no parity bit) on the drawing below.	(6 points)

b) Write the binary form of the 8 data bits received (most significant bit first).	(6 points)	01100101
 start 0 1 1 0 0 1 0 1	stop
___________________ (binary)
8) Assume the UART signal in problem 7 is sent over a RS-232 interface with drivers operating at +/- 10V. Sketch on the figure below how the signal would appear in the interface cable. The position of the start and stop bits must be aligned to the indicated positions.	(6 points)

9) We want to transmit the serial information in problems 7 and 8 at 4800 baud. What would be the values of BRGH, UxBRG, and the calculated baudrate if the PBCLK is running at 500 KHz? Pick the value of BRGH (0 or 1) that gives the calculated baudrate closest to the desired baudrate.

 BRGH = ______1______; UxBRG = __25______; calculated baudrate = 4807.69 BAUD __________ (10 points)

10) Find the even parity for the binary string 10101011	(2 points)	it’s a 1, so the string becomes 101010111

11) PIC32 interrupt IRQ number and the CPU vector number are always the same. True / False (2 points)

12) The CP0 register that determines where the ISR will “return” to is:
       Circle the correct answer - EBASE / EPC / Cause / Status / Intctl	(2 points)

13) When an ISR is entered, all registers need to be saved. True / False	(2 points) well, all registers being used that may be modified. So, not necessarily every register that exists every time.

14) If the OSCCON SFR bits COSC<2:0> = <1, 1, 1>, and FRCDIV<2:0> bits = <0, 0, 1> what is the frequency of the PIC32’s SYSCLK? ________4 MHz_______	(5 points)

15) If the PFMWS<2:0> bits of the CHECON SFR = <1, 1, 1> how many wait states have been selected? 7 wait states have been selected_______ (5 points)

16) Recall that CPU instruction execution time not only depends on the SYSCLK but also on the number of wait states programmed. Instruction execution time is (1 + #wait states) * TSYSCLK. The Cache Control Register (CHECON) configures the number of CPU wait states with the PFMWS<2:0> bits (Programmable Flash Memory Wait States). Determine the instruction execution time given the data in problems 14 and 15 above. ___2,000 ns______________________ (6 points)
clock period: 1/4*10^6 = 250 nanoseconds
(7 wait states + 1) * 250 ns = 2,000 ns

17) If Timer1 and Timer2 have the same interrupt priority and sub-interrupt priority, but they occur simultaneously, which ISR will run first? _____timer1 because it has a lower vector address.______________	(5 points)

18) Analyze the ISR code given below for Timer1. The Prologue and Epilogue have been omitted for clarity. The code’s purpose is to generate a periodic waveform on RA0. The timer’s clock is 1 MHz. Draw the approximate waveform after the system has been running for a while. Indicate the time durations of all of the high and low pulses.	(10 points)
// Prologue here – omitted	|
|
// Timer1 ISR Handler code here	|
la	t0,T1CONCLR	//stop timer	|
li	t1,0x8000	|
sw	t1,0(t0)	|
|
la t0,IFS0CLR	//clear flag	|
li t1, 0x10	|
sw t1, 0(t0)	|
la	t0, TMR1	|
sw	zero,0(t0)	|
|
la t0,PORTA	|
lw t1, 0(t0)	|
ori t1, t1, 0x0000	|
beq t1,zero,next	|
nop	|
|

la t0,PR1	|
li t1, 1000 //decimal 1000

sw t1, 0(t0)
j finish
nop

next:
la t0, PR1
li t1,2500	//decimal 2500

finish:
la	t0,T1CONSET
li	t1,0x8000
sw	t1, 0(t0)

la	t0,PORTAINV
li	t1,0x0001
sw	t1, 0(t0)

//Epilogue here – omitted

The above drawing is assuming that the code snippet given isn’t just run the single time that the snippet shows—it should be in a loop called back to back to get a waveform like that. You know, ish.

19) Determine how long the instructions below will take to execute from top: to bottom: using the instruction cycle time from question 16 above.	(10 points)

top:
li t0, 1
looping:
addiu t0, t0, -1	Execution Time = _8000 nanoseconds,	or 8 microseconds.___________________
nop
beq t0, zero, looping
nop
bottom:
//continue from here

20) What does an analog to digital converter (A/D) do?	(3 points)
it converts analog signals into digital representations. Mainly, to enable the conversion of analog signals such as voltage or current into a digital format that can be understood and processed by digital systems.

CHECON: Cache Control Register
bit 2-0 PFMWS<2:0>: PFM Access Time Defined in terms of SYSLK Wait states bits

111 = Seven Wait states
110 = Six Wait states
101 = Five Wait state
100 = Four Wait states
011 = Three Wait states
010 = Two Wait states
001 = One Wait state
000 = Zero Wait states

OSCCON Control Register
bit 26-24 FRCDIV<2:0>: Fast Internal RC Clock Divider bits

111 = FRC divided by 256
110 = FRC divided by 64
101 = FRC divided by 32
100 = FRC divided by 16
011 = FRC divided by 8
010 = FRC divided by 4
001 = FRC divided by 2 (default setting)
000 = FRC divided by 1

bit 20-19 PBDIV<1:0>: Peripheral Bus Clock Divisor
11 = PBCLK is SYSCLK divided by 8(default)
10 = PBCLK is SYSCLK divided by 4
01 = PBCLK is SYSCLK divided by 2
00 = PBCLK is SYSCLK divided by 1
Note: On Reset these bits are set to the value of the Configuration bits (DEVCFG1<13:12>)

bit 14-12 COSC<2:0>: Current Oscillator Selection bits
111 = Fast Internal RC Oscillator divided by OSCCON<FRCDIV> bits
110 = Fast Internal RC Oscillator divided by 16
101 = Low-Power Internal RC Oscillator (LPRC)
100 = Secondary Oscillator (SOSC)
011 = Primary Oscillator with PLL module (XTPLL, HSPLL or ECPLL)
010 = Primary Oscillator (XT, HS or EC)
001 = Fast RC Oscillator with PLL module via Postscaler (FRCPLL)
000 = Fast RC Oscillator (FRC)
Note: On Reset these bits are set to the value of the FNOSC Configuration bits (DEVCFG1<2:0>)